Test plan Character Card IPASS Duur Alblas V1C 2019

Hardware Requirements
To use my IPASS you need the following hardware components:
- Arduino Due
- RFID-RC522
- MIFARE 1K card type MF1S503yX
- PC/Laptop for communiction via terminal
- Connectors M/F and a USB-A to USB-Micro cable
Setup:
The following pins need to be connected as described below:
RFID-RC522	Arduino Due
SDA	PWM Pin 11
SCK	PWM Pin 8
MOSI	PWM Pin 9
MISO	PWM Pin 10
GND	GND
3.3V	3.3V

Performed tests
selfTest()
This test will show that we are successfully able to write and read to and from the RC522 chip and that the chip being used is version 2 (which is the only version supported at this time).
During this test is it necessary that we can write and read to and from the RC522 chip using the hwlib::spi_bus_bit_banged_sclk_mosi_miso’s transaction() function.
If the test completes successfully we expect to see a message saying “Chip version 2 is supported!” and the function will return rc522::status::SUCCESS.
If the test does not go as expected or the found version is not version 2 the function will return rc522::status::ERROR.

trySelect()
This test will show we can successfully select a MIFARE card and retreive the UID of said card. To show the result of this test the boolean showInfo parameter needs to be set to true.
For this test to work the previous test has to be successful. This function will try to wake up the card using a REQA or WUPA and try to select it.
If the test completes successfully we expect to see the found UID of the MIFARE card and a status SUCCESS. The function will also return a true value.
If the test does not complete successfully you will show a status (the status tries to represent where things went wrong.) And you will not see the UID. The funtion will return false.
tryAuthenticate()
This test will show we have successfully authenticated the MIFARE card block and are able to perform MIFARE Commands on said block. To show the result of this test the boolean showInfo parameter needs to be set to true.
To run this test it is necessary that the previous test have all succeeded or this test will fail. This function will try to authenticate a block with either Key A or B.
If the test completes succesfully we expect to see a SUCCESS status and the function will return true. The MIFARE card has authenticated the supplied block address. (This will be checked in the next test function.)
If the test does not complete successfully you will see a rc522::status and the function will return false. The MIFARE has not authenticated the supplied block address.
tryRead()
This function will show we can read from a MIFARE card block. To show the result of this test the boolean showInfo parameter needs to be set to true.
To run this test it is necessary that the previous test have all succeeded or this test will fail. This function will send a read command to the MIFARE card and store the response.
If the test completes successfully we expect to see a SUCCESS status and the function will return true. The MIFARE card block is read and the function prints the received data.
If the test does not complete successfully you will see a rc522::status and the function will return false. And the function will print the data that is in the buffer the user supplied.
TryWrite()
This function will show we can write to a MIFARE card block. To show the result of this test the boolean showInfo parameter needs to be set to true.
To run this test it is necessary that the previous test have all succeeded or this test will fail (except the tryRead() function). This function will send a write command to the MIFARE card and send the buffer the user supplied to the MIFARE card.
If the test completes successfully we expect to see a SUCCESS status and the function will return true. The MIFARE card block is written.
If the test does not complete successfully you will see a rc522::status and the function will return false.
demo()
This test will show that we can select, authenticate, read and write from a block. To show the result of this test the boolean showInfo parameter needs to be set to true.
To run this test it is necessary that the previous test have all succeeded or this test will fail. This function will select a MIFARE card, try to authenticate a block with a supplied key and then read from the block. Next it will write the supplied buffer to the block and read the written info. Lastly it will use the stopCrypto() function to tell the RC522 chip that we have finished communicating with the MIFARE card.
If the test completes successfully we expect to see several SUCCESS statuses. We will also see the data read and newly written data.
If the test does not complete successfully we expect to see either some SUCCESS statuses or none and the returned rc522::status’s from the previous functions.
My process
I have tested my setup in a lot of ways since the start of the project.
First I started off by trying to get a response from the RC522 chip, after struggling to get a response for 2 days I decided to read what I was sending to my RC522 chip using the Analyzer and the Saleae software. I Found out my NSS (or SDA) line was inverted. After fixing said problem I started to get responses from the RC522 chip.
Next I wrote a series of tiny tests to test the connection and functionality of the hwlib spi_bus_bit_banged_sclk_mosi_miso and it’s transaction() function. These tests have become unusable and thus removed from the repository.
After some trail and error I managed to finally write to the FIFO buffer of my RC522 chip. I started to implement the supplied self test functionality of the chip. This self test function is still available and even being run every time a user starts up the program. This test also checks the version of the chip that’s being used. I made a function to compare the found version of the chip to the responses found in the documentation of the chip. Since I wrote this library solely for the second version (for now) I implemented a test that will shut down the program if the used chip is not version 2 (see the selfTest() and compareVersion() functions).
Next I started to figure out the process of accessing a MIFARE card. This took a long time since the documentation on these cards is (in my opinion) not very well done. After I figured out that the REQA and WUPA commands need to be formatted in a 7 bit frame using the functionality of the RC522 chip things started to look up. I wrote several test functions for each step in the process of trying to read and write to and from the MIFARE card. These functions are still in the repository and are being used in a demo() function that can be used to demonstrate the trySelect(), tryAuthenticate(),tryRead and tryWrite() functions.
After writing the basis for my application I started to write some test functions to test the functionality of my application. The testSheet() function is still avaiable and being used to generate a pre-made character on startup of the application. Then I wrote some basic functionality functions to demonstrate the write and read capabilities using the sheet. I’ve asked several people to test my application for me and (even though it’s not completely fool proof) it works well and the users could create, write and read their sheets.
Over the course of creating this library I wrote a lot of tiny test functions a lot of which have been removed for the sake of security. After I had been taught how to use enum’s I decided to make almost all of my functions more secure by using these enum classes. This not only made sure users of this library can’t just use magic numbers but it also helped me return meaningful statuses. From then on I could write my functions with build in tests so I received a meaningful status when things went correctly, or not, instead of magic numbers.

Known limits / problems
Since communication with a MIFARE card is quite complex I lost a lot of time implementing this correctly. This resulted in the fact that I had less time to work on advanced functionalities. It is for this reason that the user input is not fool proof. A user can neglect to input values when asked for them or input values which are , for example, too large in case of numbers. Since every type of communication is being handled by functions a user can’t write to places like the block where the key’s and accessibility bits are stored. If a user decides to write his own functions using my library he could in theory write to those blocks and brick the card and making them unusable because I have not made function to check which blocks are being written to. In the future I could implement functions that would restrict the blocks where a user is allowed to write to and I could implement functions that would allow a user to set key’s and accessibility bits safely. The reason I did not implement this now is not because I cannot write to these blocks but because I have not been able to implement this in a safe way where I can guarantee a user will not brick his/her card in the time I had left.